## Slide 1: HarNice!
The free, open-source electrical system design tool.

## Slide 2: Disclaimer
I wrote this in past tense, but it’s far from done!
This is my first-ever real coding project
  I don’t claim that my implementation is any good – just judge my approach!
I’ve never truly used another real systems engineering tool
  Maybe I’m reinventing a wheel
  Maybe we can steal all their business by making the first free and open source electrical systems engineering tool

## Slide 3: What is an electrical system?
Any collection of circuit boards, devices, other things, that connect to each other with wires or harnesses
Requires engineering trades and decisions to design
Examples:
  Concert sound system
  Avionics system on a rocket or satellite
  Commercial power distribution system
  iPhone
Vehicle computer
Actuator controller
Power distribution unit
Battery
Actuator
Network switch
Sensor DAC unit
Pressure sensor
Pressure sensor
Pressure sensor

## Slide 4: What is not an electrical system? (from the perspective of HarNice)
Specifics of the electrical behavior going on inside a device
  We take the assumption that any device has inputs and outputs and what it does to relate the two is not part of “system engineering”
  It’s okay to simplify what a box does as long as it does not jeopardize your understanding of its external functionality
Network routing
  Software configs are agnostic to the electrical systems
How your electrical hardware interacts with non-electrical things
  We don’t care about g-loading, what kind of fluid your sensors are measuring, etc

## Slide 5: How do you design your system right now?
The competition:
  Zuken, E-plan, etc
  SUPER expensive, cumbersome, training-intensive
Pen and paper vibes: hardly better than graph paper
Alternatively, Vizio, Powerpoint, Excel, MS Paint
  No metadata in your drawings
  No enforceable design rule checks
  Conflicting sources of truth
  Required manual dependencies
  No centralized revision control

## Slide 6: Harnice solves this.
There can and should always exist one single source of truth for any entire electrical system.
On the assumption that the following are known, every artifact (harness drawing, BOM, etc) should be fully deterministic.
  Your system is fully defined
    You know how many devices you need and how you want them to be connected
  You have complete details about how each device works
    Device connectors and channels are fully defined
  Every design standard you adhere to is expressible
    Ex. “We always put yellow heat shrink if the harness contains a signal with this name”
    Ex. “Every time a harness contains more than two receptacle connectors, switch the font size on the label”
  The physical routing of a harness can be imported or asserted
    Harnice doesn’t know how long a harness needs to be

## Slide 7: How do you know what to design?
Traditionally, the engineer compiles information either from a design guide, from industry knowledge, or other sources,
  …manually…
until their design is complete.
INSTEAD:
Harnice encourages the user NOT to compile any information, and instead, explicitly document your design standards and rules in a machine-readable format.
Let the machines work for you!

## Slide 8: High-level requirements
Harnice shall have just one command which should update everything about a product
Harnice shall allow users to input their design rules using a well-known human-readable language
Harnice may only produce ONE deterministic solution to any product, and raise an error if multiple or zero solutions are found
Harnice shall not operate on released parts`

## Slide 9: Flexibility requirements
If you can define something as an “instance” with “attributes”, it should be able to end up in a harness build file.
Harnice shall minimize the number of terms that represent physical goods. The terms “connector” or “cable” don’t inherently mean anything

## Slide 10: The solution
You specify your system using Kicad or Altium
  Components represent devices
  Nets represent harnesses
Harnice runs a bunch of code on your netlist to determine harness requirements
  Builds a channel map
  Builds a System Instances List (list of every part and every connection for every harness)
Harnice harness editor can look for a harness inside a system
  Adds parts based on standard build rules
  Exports build drawings and other artifacts instantaneously
Kicad
Netlist
Device definitions
Channel map
Channel definitions
System instances list
Company build rules
Harness instances list
Harness drawing
Artifact build rules
done
In prog
todo

## Slide 11: a word on terminology…

## Slide 12
Term | Description | Scope | Attributes | Examples
“System” | A complete overview of every relevant piece of hardware in your system | Systems contain devices and nets | Which device part numbers and how many are you using How each device is connected to each other | Vehicle HITL Test stand Concert sound system Residential AC power distribution
“Device” | A physical device that interfaces with other devices via hardware electrical signals |  | Part number Connectors Channels | Pressure sensor ADC Light switch MacBook
“Channel” | A set of signals | Devices have Channels Channels exist in a centralized library Channels are not allowed across multiple connectors yet | Other compatible channels Input, output, or both Range, tolerance Data format | “Power in” “Mic level signal” FTT (4-20mA) 500mHz 50ohm
“Signal” | An individual conductor going in or out of a device | Channels are defined to contain Signals Device Connectors must contain all device Channels’ Signals | Signal name | +5V Chassis CS, MISO, MOSI
“Net” | A set of connectors | Nets defined at the system-level Nets are not harness part numbers | Which connectors of which devices are included in the net | N$1
“Harness” | A physical device that exists to link devices together | Harnesses contain Circuits and mating connectors | Harness part number Contained parts | Lightning cable Your favorite octopus harness
“Circuit” | A connection between one signal and another | Circuits contain contacts, conductors, etc that form an electrical path | Name | Channel 1 +5V

## Slide 13: The Harnice workflow
harnice –r harness
harnice –r system
harnice –r device
User editable per product
Generated file
System Definition (kicad_sch)
System Instances List
Harness feature tree
System Feature Tree
Device Feature Tree
Device Signals List
Device Kicad Symbol
Harness Instances List
Harness Build Drawing PDF set
When you “render” a product (run harnice –r <product> from the command line), the feature tree is called
Feature Tree pulls from existing information, processes it, and makes artifacts

## Slide 14: Harnice products
 | System | Harness | Device | Part | Title block | Flagnote
Inputs (existing information) | Netlist exported from Kicad or Altium | System instances list, manual YAML or JSON harness definition | ICD.py |  | Params.json | Params.json
Generated outputs | Instances list.tsv | Instances list.tsv | Signals list.tsv .Kicad_sym | Attributes.json Drawing.svg | Attributes.json Drawing.svg | Drawing.svg
When you “render” a product, inputs are converted to outputs

## Slide 15
Harnice workflow – for systems
harnice --render system
System instances list
Part number feature_tree.py
Prebuilder .py
Prebuilder .py
Prebuilder .py
User editable per product
Harnice module
Import from library
Generated file
Netlist from Kicad
Your preferences for mating connectors
Channel map assignment instructions
System instances list
System instances list
Prebuilder .py
Weird rules you might need
System instances list

## Slide 16: Feature Tree
harnice --render <product>
Input file(s) if relevant
Output file
Part number feature_tree.py
Build macro
Output macro
Build macro
Build macro
Output file
Output macro
Output file
Output macro
User editable per product
Harnice module
Import from library
Part(s) if relevant
Flagnotes, tblocks if relevant
Generated file
System instances list if relevant
Product data structure
Regardless of which product you’re working on, when you call “render”, harnice will run “featuretree.py”
Feature Tree, notionally based on Solidworks, will sequentially build up the product’s data structure based on “prebuilders” you can write and select
Feature Tree will also call Artifact Builders, which do stuff like generate a BOM, make a PDF drawing, etc
Example of inputs
Example of outputs

## Slide 17: Harnice workflow – for harnesses
harnice --render system
Harness instances list
Part number feature_tree.py
Prebuilder .py
Prebuilder .py
Prebuilder .py
System instances list
Your weird build rules for this project
Your company’s build rules
Harness instances list
Harness instances list
Artifact builder .py
PDF drawing
Artifact builder .py
BOM
Artifact builder .py
Vdrop calcs idk
User editable per product
Harnice module
Import from library
Generated file

## Slide 18: System Feature Tree Example

## Slide 19: Macros
A macro is a chunk of Python that has access to your project files or any other Python-capable function
When you call featuretree_utils.run_macro(), it will import the macro from a library and run it in your script
Some macros are designed to be used to build systems, build harnesses, or export contents “artifacts” from a harness instances list
Macros I currently have written in the public library

## Slide 20: Build Macros
Intended to add or modify lines on an instances list based on a standard set of rules or instructions
  Can read information from the instances list
  Can read information from other support files
Examples
  featuretree.runprebuilder(“wireviz_yaml_prebuilder”, “public”)
    Reads a wireviz YAML (another commonly used harness design format)
  featuretree.runprebuilder(“add_yellow_htshrk_to_plugs”, “kenyonshutt”)
    You can write any rule or set of rules you want in Python, save it to your library, and call it from a harness feature tree.
    This one, for example, might scour the instances list:
      for plug in instances_list:
        if item_type==plug:
          instances_list.add(heatshrink, to cable near plug)

## Slide 21: Outputs
Output Macros will scour the Instances List or other artifact outputs and make other things out of it
  BOM
  Formboard arrangement
  PDF drawing sheet
  Analysis calcs
  Write your own!

## Slide 22: Data structure: “instances_list.tsv”
  A list of every single item, idea, note, part, instruction, circuit, literally anything that comprehensively describes how to build that harness or system
  TSV (tab-separated-values, big spreadsheet)
  Declined alternatives: STEP files, schematics, dictionaries not general, descriptive, or human readable enough

## Slide 23: Harness Instances List example

## Slide 24: Libraries
Parts, macros, titleblocks, flagnotes, etc, should be re-used and referenced for any future use
Users are heavily encouraged to contribute to the public git repo for your cots parts
  harnice-library-public
However, you can define paths to as many library repos as you want.
  my-company-harnice-library
  my-super-top-secret-harnice-library
You don’t even have to use git to control it if you don’t want!

## Slide 25: Product version control
To “render” a product (harness, part, etc) with Harnice, the CLI will force you to operate in a “rev folder”
Revision data always stored in revision_history.tsv
Harnice will not render a revision if there’s data in the “status” field, i.e. “released” or “outdated”
Revision information can be referenced elsewhere, ex in pdf_generator

## Slide 26: Library flexibility
All parts in a library are version controlled per previous slide…
When importing an item from library, you can request different versions or overwrite imported libraries flexibly…
revision_history.tsv to track all revisions of a product
User-editable copy (instances_list tracks “modified” from imported library)
Library will be imported new at every Render for traceability purposes
Different instances, even with the same MPN, are imported separately
All imported items work the same way

## Slide 27: Show me what you can do!
Here’s an output from a macro called “pdf_generator”.
It compiled the outputs of other output macros like “harnice standard formboard builder”, “bom to svg”, “buildnotes to svg”
It knows the scale, the location, the buildnotes you need, what your parts look like, the revision history, all from the information on the Instances List

## Slide 28
Another page shows a 1:1 scale view on a 8.5”x11” sheet.
Connectors and backshells shown here are just rectangles, but could easily be photos or CAD screenshots.
Flagnote positions are not well-defined, but can be configured as needed.

## Slide 29
Pages can be edited with your favorite SVG editor…

## Slide 30
Of course…
All output artifacts are perfectly in sync with the Instances List

## Slide 31
Every part can have as many child coordinate systems as you need
These can be referenced in the instances list
Used for things like flagnotes, child parts, or other related items
Can be used to place parts on a formboard drawing, calculate distances, etc

## Slide 32
Defining a physical layout
For now, formboard_definition.tsv allows user to input length and angle preferences
These sync with cables and requirements from instances_list
Eventually, I’ll make a GUI