## Slide 1: HarNice!
The free, open-source electrical system design tool.

## Slide 2: Disclaimer
I wrote this in past tense, but it’s far from done!
This is my first-ever real coding project
  I don’t claim that my implementation is any good – just judge my approach!
I’ve never truly used another real systems engineering tool
  Maybe I’m reinventing a wheel
  Maybe we can steal all their business by making the first free and open source electrical systems engineering tool
DO NOT USE THIS SLIDESHOW FOR HOW-TO ADVICE. INFO AND TERMINOLOGY CHANGED QUCKLY WHILE I WAS DRAFTING THIS PRESENTATION.

## Slide 3: What is an electrical system?
Any collection of circuit boards, devices, other things, that connect to each other with wires or harnesses
Requires engineering trades and decisions to design
Examples:
  Concert sound system
  Avionics system on a rocket or satellite
  Commercial power distribution system
  iPhone
Vehicle computer
Actuator controller
Power distribution unit
Battery
Actuator
Network switch
Sensor DAC unit
Pressure sensor
Pressure sensor
Pressure sensor

## Slide 4: What is not an electrical system? (from the perspective of HarNice)
Specifics of the electrical behavior going on inside a device
  We take the assumption that any device has inputs and outputs and what it does to relate the two is not part of “system engineering”
  It’s okay to simplify what a box does as long as it does not jeopardize your understanding of its external functionality
Network routing
  Software configs are agnostic to the electrical systems
How your electrical hardware interacts with non-electrical things
  We don’t care about g-loading, what kind of fluid your sensors are measuring, etc

## Slide 5: How do you design your system right now?
The competition:
  Zuken, E-plan, etc
  SUPER expensive, cumbersome, training-intensive
Pen and paper vibes: hardly better than graph paper
Alternatively, Vizio, Powerpoint, Excel, MS Paint
  No metadata in your drawings
  No enforceable design rule checks
  Conflicting sources of truth
  Required manual dependencies
  No centralized revision control

## Slide 6: Harnice solves this.
There can and should always exist one single source of truth for any entire electrical system.
On the assumption that the following are known, every artifact (harness drawing, BOM, etc) should be fully deterministic.
  Your system is fully defined
    You know how many devices you need and how you want them to be connected
  You have complete details about how each device works
    Device connectors and channels are fully defined
  Every design standard you adhere to is expressible
    Ex. “We always put yellow heat shrink if the harness contains a signal with this name”
    Ex. “Every time a harness contains more than two receptacle connectors, switch the font size on the label”
  The physical routing of a harness can be imported or asserted
    Harnice doesn’t know how long a harness needs to be

## Slide 7: How do you know what to design?
Traditionally, the engineer compiles information either from a design guide, from industry knowledge, or other sources,
  …manually…
until their design is complete.
INSTEAD:
Harnice encourages the user NOT to compile any information, and instead, explicitly document your design standards and rules in a machine-readable format.
Let the machines work for you!

## Slide 8: High-level requirements
Harnice shall have just one command which should update everything about a product
Harnice shall allow users to input their design rules using a well-known human-readable language
Harnice may only produce ONE deterministic solution to any product, and raise an error if multiple or zero solutions are found
Harnice shall not operate on released parts`

## Slide 9: Flexibility requirements
If you can define something as an “instance” with “attributes”, it should be able to end up in a harness build file.
Harnice shall minimize the number of terms that represent physical goods. The terms “connector” or “cable” don’t inherently mean anything

## Slide 10: The solution
You specify your system using Kicad or Altium
  Components represent devices
  Nets represent harnesses
Harnice runs a bunch of code on your netlist to determine harness requirements
  Builds a channel map
  Builds a System Instances List (list of every part and every connection for every harness)
Harnice harness editor can look for a harness inside a system
  Adds parts based on standard build rules
  Exports build drawings and other artifacts instantaneously
Kicad
Netlist
Device definitions
Channel map
Channel definitions
System instances list
System Feature Tree
Harness instances list
Harness drawings
Harness Feature Tree

## Slide 11: a word on terminology…

## Slide 12
Term | Description | Scope | Attributes | Examples
“System” | A complete overview of every relevant piece of hardware in your system | Systems contain devices and nets | Which device part numbers and how many are you using How each device is connected to each other | Vehicle HITL Test stand Concert sound system Residential AC power distribution
“Device” | A physical device that interfaces with other devices via hardware electrical signals |  | Part number Connectors Channels | Pressure sensor ADC Light switch MacBook
“Channel” | A set of signals | Devices have Channels Channels exist in a centralized library Channels are not allowed across multiple connectors yet | Other compatible channels Input, output, or both Range, tolerance Data format | “Power in” “Mic level signal” FTT (4-20mA) 500mHz 50ohm
“Signal” | An individual conductor going in or out of a device | Channels are defined to contain Signals Device Connectors must contain all device Channels’ Signals | Signal name | +5V Chassis CS, MISO, MOSI
“Net” | A set of connectors | Nets defined at the system-level Nets are not harness part numbers | Which connectors of which devices are included in the net | N$1
“Harness” | A physical device that exists to link devices together | Harnesses contain Circuits and mating connectors | Harness part number Contained parts | Lightning cable Your favorite octopus harness
“Circuit” | A connection between one signal and another | Circuits contain contacts, conductors, etc that form an electrical path | Name | Channel 1 +5V

## Slide 13: The Harnice workflow
harnice –r harness
harnice –r system
harnice –r device
User editable per product
Generated file
System Definition (kicad_sch)
System Instances List
Harness feature tree
System Feature Tree
Device Feature Tree
Device Signals List
Device Kicad Symbol
Harness Instances List
Harness Build Drawing PDF set
When you “render” a product (run harnice –r <product> from the command line), the feature tree is called
Feature Tree pulls from existing information, processes it, and makes artifacts

## Slide 14: Harnice products
 | System | Harness | Device | Part | Title block | Flagnote | Channel Types
Inputs (existing information) | Netlist exported from Kicad or Altium | System instances list, manual YAML or JSON harness definition | ICD.py |  | Params.json | Params.json | 
Generated outputs | Instances list.tsv | Instances list.tsv | Signals list.tsv .Kicad_sym | Attributes.json Drawing.svg | Attributes.json Drawing.svg | Drawing.svg | 
When you “render” a product, inputs are converted to outputs
Update

## Slide 15
Harnice workflow – for systems
harnice --render system
System bom
Part number feature_tree.py
Kicad to bom macro
User editable per product
Harnice module
Import from library
Generated file
Netlist from Kicad
Your channel map preferences
Your disconnect map preferences
Weird macros you might want
Weird rules you might need
Import parts from library
Make connector list
Connectors list
Make channel map
Channel map
Make disconnect map
Disconnect map
Make circuits list
Circuits list
Make instances list
System Instances list

## Slide 16: Feature Tree
harnice --render <product>
Input file(s) if relevant
Output file
Part number feature_tree.py
Build macro
Output macro
Build macro
Build macro
Output file
Output macro
Output file
Output macro
User editable per product
Harnice module
Import from library
Part(s) if relevant
Flagnotes, tblocks if relevant
Generated file
System instances list if relevant
Product data structure
Regardless of which product you’re working on, when you call “render”, harnice will run “featuretree.py”
Feature Tree, notionally based on Solidworks, will sequentially build up the product’s data structure
Feature Tree will also call macros, which do stuff like generate a BOM, make a PDF drawing, etc
Example of inputs
Example of outputs

## Slide 17: Harnice workflow – for harnesses
harnice --render system
Harness instances list
Part number feature_tree.py
Build macro
Build macro
Build macro
System instances list
Your weird build rules for this project
Your company’s build rules
Harness instances list
Harness instances list
Output macro
PDF drawing
Output macro
BOM
Output macro
Vdrop calcs idk
User editable per product
Harnice module
Import from library
Generated file
Flowchart?

## Slide 18: System Feature Tree Example

## Slide 19: Channel Types
Refer to a channel type as
channel_type = (channel_type_id, repo)
Represents a type of channel that is compatible with other channels of similar types that can be mapped to each other.

## Slide 20: Macros
A macro is a chunk of Python that has access to your project files or any other Python-capable function
When you call featuretree_utils.run_macro(), it will import the macro from a library and run it in your script
Some macros are designed to be used to build systems, build harnesses, or export contents “artifacts” from a harness instances list
Macros I currently have written in the public library

## Slide 21: Build Macros
Intended to add or modify lines on an instances list based on a standard set of rules or instructions
  Can read information from the instances list
  Can read information from other support files
Examples
  featuretree.runmacro(“import_wireviz_yaml”, “public”)
    Reads a wireviz YAML (another commonly used harness design format)
  featuretree. runmacro(“add_yellow_htshrk_to_plugs”, “kenyonshutt”)
    You can write any rule or set of rules you want in Python, save it to your library, and call it from a harness feature tree.
    This one, for example, might scour the instances list:
      for plug in instances_list:
        if item_type==plug:
          instances_list.add(heatshrink, to cable near plug)

## Slide 22: Signals Lists
Signals Lists are the primary way Harnice stores information about devices
Source of truth for devices or disconnects
Exhaustive list of every electrical connection going into or out of the device or disconnect
Device signals list (for Shure SM58 microphone)
Disconnect signals list (for a bespoke audio use case)

## Slide 23: Rules about Signals Lists
Every combination of (channel_id, signal) must be unique within the signals list
  You can’t have two “ch1, pos” signals on the same device
Every signal of a channel_type must be present in the Signals List
  If your channel_type requires “positive” and “negative”, you have to have both in your signals list
Every signal in the Signals List must be present in the channel_type
  If you need to add signals that aren’t already part of your pre-defined channel_type, you’ll need to define a new channel_type.
You can’t put signals of the same channel on different connectors
  While this may sound convenient, it breaks a lot of internal assumptions Harnice is making on the back end about how to map channels.
  If you need to do this, I recommend defining one channel type per signal, then write a macro for mapping the channels to their respective destinations.
“A” and “B” channels of the same disconnect must be compatible with each other

## Slide 24: Signals List Fields
Device signals list
Disconnect signals list
channel_id | signal | A_cavity | B_cavity | A_connector_mpn | A_channel_type | B_connector_mpn | B_channel_type
Unique name of the channel that this signal is part of | Electrical signal “positive”, “TX”, etc | Cavity name of where this signal lands on the “A” side of this disconnector | Usually the same as “A” cavity if the connectors are compatible | Be specific, this may directly end up in your BOM later | Intended purpose, mate, and map compatibility is contained here |  | Not necessarily the same as “A_channel_type” because one side of disconnect is usually “input” and the other is “output”
channel_id | signal | connector_name | cavity | connector_mpn | channel_type
Unique name of the channel that this signal is part of | Electrical signal “positive”, “TX”, etc | Name of the connector | Cavity name of where this signal lands on your device | Be specific, this may directly end up in your BOM later | Intended purpose, mate, and map compatibility is contained here
signals_list.write_signal()

## Slide 25: Signals List Feature Tree
You can use a script to easily write long Signals Lists. Rely on basic Python to avoid typing manually.
harnice -r device
Or
harnice -r disconnect
Signals List Exists
Feature Tree Exists
Make new feature_tree.py from default
no
no
Run feature_tree.py
yes
Feature Tree Exists
Validate and exit
yes
yes
no

## Slide 26: KiCad Integration
When you render a device Signals List, it’ll make a KiCad schematic symbol in the parent directory
KiCad Symbol will contain ports that match the set of connectors that you’ve specified in Signals List
Render will not affect placement or graphic design of your symbol, just port count and symbol attributes

## Slide 27: Signals List Lightweight Render
If you need to build a KiCad block diagram quickly, without specifying channels and signals, you can with --lightweight.
Run harnice -l device or harnice --lightweight device from your device directory.
This will follow the same flowchart as --render, but truncate the validation process.
You will not be able to map channels with --lightweight

## Slide 28: Signals List Python Commands
Command | Args | Returns | Purpose
signals_list.new_list() |  |  | Create a new list
signals_list.write_signal() | See earlier slides on what’s required and why |  | Add a signal to a signals list
signals_list.signals_of_channel_type() | Channel type in touple form (channel_type_id, repo) *One arg, in parenthesis* | List of all the signals of that channel type | Use to validate that you’ve specified all the necessary channels when constructing a signals list
signals_list.compatible_channel_types() | Channel type in touple form (channel_type_id, repo) | List of touples of all other compatible channel types | See if a channel in question is compatible with another channel
signals_list.cavity_of_signal() | channel_id (what channel are you looking for) signal (what signal are you looking for) path_to_signals_list (where are you looking for it at) | Cavity | Quickly find which cavity a signal of a channel lands on in a specific device
signals_list.connector_name_of_channel() | channel_id (what channel are you looking for) path_to_signals_list (where are you looking for it at) | Connector name | Quickly find which connector a channel exists on in a specific device
signals_list.path_of_channel_type() | Channel type in touple form (channel_type_id, repo) | Local path to a channel_types spreadsheet | Given a channel_type touple, find the local path to its source-of-truth channel types list
signals_list.parse_channel_type() | Channel type in touple form (channel_type_id, repo) | list of size 2: [int channel type id, | Given a channel_type touple, split it into parsed values that are easy to interact with

## Slide 29: Data structure: “instances_list.tsv”
  A list of every single item, idea, note, part, instruction, circuit, literally anything that comprehensively describes how to build that harness or system
  TSV (tab-separated-values, big spreadsheet)
  Declined alternatives: STEP files, schematics, dictionaries not general, descriptive, or human readable enough

## Slide 30: Harness Instances List example

## Slide 31: Local Paths vs Traceable URLs
Fill out

## Slide 32: Harnice Code Repo Structure
Harnice
  Lists
  Products
  Utils
  cli.py
  fileio.py
Functions that interact directly with project files (tsv, csv, …)
Use for writing your own lower level scripts and macros
Mostly <product>.render() with some exceptions
High level functions
Handles command line interface
Handles file structure

## Slide 33: Libraries
Parts, macros, titleblocks, flagnotes, etc, should be re-used and referenced for any future use
Users are heavily encouraged to contribute to the public git repo for your cots parts
  harnice-library-public
However, you can define paths to as many library repos as you want.
  my-company-harnice-library
  my-super-top-secret-harnice-library
You don’t even have to use git to control it if you don’t want!

## Slide 34: Product version control
To “render” a product (harness, part, etc) with Harnice, the CLI will force you to operate in a “rev folder”
Revision data always stored in revision_history.tsv
Harnice will not render a revision if there’s data in the “status” field, i.e. “released” or “outdated”
Revision information can be referenced elsewhere, ex in pdf_generator

## Slide 35: How to Make Outputs!
Output Macros will scour the Instances List or other artifact outputs and make other things out of it
  BOM
  Formboard arrangement
  PDF drawing sheet
  Analysis calcs
  Write your own!

## Slide 36: Library flexibility
All parts in a library are version controlled per previous slide…
When importing an item from library, you can request different versions or overwrite imported libraries flexibly…
revision_history.tsv to track all revisions of a product
User-editable copy (instances_list tracks “modified” from imported library)
Library will be imported new at every Render for traceability purposes
Different instances, even with the same MPN, are imported separately
All imported items work the same way

## Slide 37: PDF Generator
imported_instances
Library_used_do_not_edit
instance_data
Harness rev folder
Project titleblock folders
{Macro that called it}-
{page number}-
{page name}
{macro id}-{page name}-attributes.json
Macro
{Macro ID}
Page_setup.json
Titleblock
Macro-{macro ID}-{page name}
direct_from_project_titleblock
Master contents svg
Output PDF
Project titleblock files
{macro id}-{page name}-drawing.svg
{macro id}-{page name}-attributes.json
Macro titleblock files
{macro id}-{page name}-drawing.svg
{macro id}-{page name}-drawing_with_text_replacements.svg
Page_svgs
{page_counter}-{page name}-user editable.svg
Titleblocks in library repo
This is the notional flow of SVG content when you run the PDF generator macro.
1. Import titleblock content into project
2. Copy into macro directory
1.5 User can edit titleblocks directly here
3. Text replacements automatically performed (adds page number, pn/rev, etc)
Literally any file that ends in –master.svg
4. Go find all generated content
5. Merge into user editable page svg
5. Merge into user editable page svg
6. Combine into output PDF
5.5 User can configure page content and layout here by cloning master contents groups and placing the clones on the page

## Slide 38: Show me what you can do!
Here’s an output from a macro called “pdf_generator”.
It compiled the outputs of other output macros like “harnice standard formboard builder”, “bom to svg”, “buildnotes to svg”
It knows the scale, the location, the buildnotes you need, what your parts look like, the revision history, all from the information on the Instances List

## Slide 39
Another page shows a 1:1 scale view on a 8.5”x11” sheet.
Connectors and backshells shown here are just rectangles, but could easily be photos or CAD screenshots.
Flagnote positions are not well-defined, but can be configured as needed.

## Slide 40
Pages can be edited with your favorite SVG editor…

## Slide 41
Of course…
All output artifacts are perfectly in sync with the Instances List

## Slide 42
Every part can have as many child coordinate systems as you need
These can be referenced in the instances list
Used for things like flagnotes, child parts, or other related items
Can be used to place parts on a formboard drawing, calculate distances, etc

## Slide 43
Defining a physical layout
For now, formboard_definition.tsv allows user to input length and angle preferences
These sync with cables and requirements from instances_list
Eventually, I’ll make a GUI